## Slide 1: BCM Functions

## Slide 2
Interview Answer: “Explain BCM Functions and How It Works”
Sample Answer (Well-Structured for Interviews):
“BCM stands for Body Control Module.
It’s one of the main ECUs in the vehicle that controls most of the body electronics and comfort functions like lighting, wipers, central locking, alarm, seat belt reminder, and remote keyless entry.
The BCM receives input signals from switches, sensors, and other ECUs through CAN/LIN communication, processes them according to logic, and sends output commands to actuators or relays to perform required actions.”

## Slide 3
1. Exterior Lamp Control
BCM controls all exterior lights — headlamps, tail lamps, DRLs, etc.
Based on the light switch and ambient light sensor, it decides which lamps to turn ON/OFF.
Example:
--> In AUTO mode, BCM automatically switches ON low-beam and tail lamps in dark conditions.
--> In daylight, BCM activates DRL (Daytime Running Lamp) instead of low-beam.
Inputs: Light switch position, ambient light sensor, ignition.
Outputs: Lamp relays or LIN messages to lighting modules.
2. Wiper Control
BCM manages the front and rear wipers through signals from the wiper stalk or rain sensor.
Modes include OFF, MIST, INIT, LOW, HIGH.
In AUTO mode, rain sensor data controls wiping speed automatically.
INIT ensures blades move to park position after ignition ON.
➡️ Inputs: Wiper stalk, rain sensor, hood switch.
➡️ Outputs: Wiper motor control via relay or LIN.

## Slide 4
3. Central Door Lock/Unlock
BCM locks/unlocks all doors based on RKE (Remote Key Entry), door switch, or vehicle speed.
Supports features like auto lock (above 20 km/h) and crash unlock (after airbag deployment).
It ensures safety interlocks — for example, it may prevent locking if any door is open.
➡️ Inputs: Door switches, speed signal, crash input.
➡️ Outputs: Door lock actuator signals.
4. Burglar Alarm (B/Alarm)
BCM activates horn and hazard lamps when unauthorized entry is detected.
System arms when locked via RKE and disarms on unlock or ignition ON.
If a door or hood is opened without disarming, the alarm triggers.
➡️ Inputs: Door/hood/trunk switches, RKE lock/unlock.
➡️ Outputs: Horn relay, hazard lamp control.

## Slide 5
5. Seat Belt Reminder (SBR)
BCM monitors seat occupancy and buckle switch to remind driver/passenger to fasten belts.
When the seat is occupied and the belt is not fastened with ignition ON, it activates a buzzer and warning lamp.
➡️ Inputs: Seat occupancy sensor, buckle switch, ignition.
➡️ Outputs: Warning indicator, buzzer.
6. Remote Keyless Entry (RKE)
BCM receives wireless RF signals from the key fob for Lock, Unlock, and Panic.
Based on the command:
  Lock: Locks doors and arms alarm.
  Unlock: Unlocks doors and disarms alarm.
  Panic: Activates horn and hazard lamps for emergency alert.
Communication happens between RKE receiver → BCM → actuators.
➡️ Inputs: RKE receiver (Lock/Unlock/Panic commands).
➡️ Outputs: Door lock actuators, horn, hazard lamps.

## Slide 6
Short Summary Version (for a quick interview response):
“BCM acts as the brain for body electronics. It collects input signals like light switch, wiper stalk, door status, and remote key signals through CAN or LIN, processes logic internally, and controls outputs like lamps, wipers, locks, horn, and buzzers.
It ensures comfort, convenience, and safety features such as automatic lighting, rain-sensing wipers, central locking, burglar alarm, seat belt reminder, and RKE.
I’ve tested these BCM functions using CANoe and VT System on HiL setup by simulating input conditions and verifying correct output responses and CAN messages.”