## Slide 1: SMK Functions

## Slide 2
Function Overview
Passive Unlock: When the user approaches the vehicle with the key and touches the door handle sensor, the SMK detects the key via PE (Passive Entry) antennas and unlocks the door automatically.
Passive Lock: When the user leaves the vehicle with the key and touches the lock sensor on the handle, SMK ensures the key is outside and locks all doors.
Passive Trunk: Similar logic; trunk opens when the key is near the rear antenna and the trunk switch is pressed.
Working Logic
Approach: LF antennas send challenge → Key responds via RF → authentication OK → BCM unlocks.
Departure: LF antenna detects key outside → user touches lock sensor → lock command sent.

## Slide 3
Immo (Immobilizer)
Overview
Prevents engine start with unauthorized keys.
SMK and ECM exchange cryptographic authentication data (Key ID / Rolling code).
If authentication fails → ECM blocks fuel injection and cranking.
SSB (Start Stop Button) Function
Overview
Enables ignition ON/OFF and engine start without physical key insertion.
Based on key authentication and brake (or clutch) input.
Logic:
Key inside cabin + Brake applied + SSB pressed → Start authorization → EMS enables crank.
Key not detected → Start not allowed.
Ignition OFF by pressing SSB again.

## Slide 4
Puddle Pocket Lamp
Overview
Small light under the door mirror illuminates ground area when user approaches vehicle or unlocks it.
Triggered by Passive Unlock or RKE Unlock.
ESCL (Electronic Steering Column Lock)
Overview
Locks or unlocks steering column electronically for security.
When key authentication success → unlock ESCL for driving.
When ignition OFF and door locked → lock ESCL.

## Slide 5
Welcome Mirror Fold / Unfold
Overview
When the user approaches the car (Passive Unlock) → Mirrors automatically unfold.
When user locks and leaves → Mirrors fold automatically (Welcome/Goodbye feature).
Warning Functions
a) Door Lock Warning
If a lock command is issued while any door is open → SMK sends warning (buzzer or cluster message).
Prevents locking the vehicle with a door open.
b) Trunk Warning
Triggered when trunk is not fully closed and user tries to lock the vehicle.BCM or SMK prevents lock and triggers buzzer.
c) Key Out Warning
If key is removed from cabin while ignition ON or driver door open, SMK triggers warning.Ensures driver doesn’t leave car running with key outside.
d) Auth Fail Warning
If SMK fails to authenticate key during passive unlock/start, “Key Not Detected” or “Auth Fail” message shown.

## Slide 6
The Smart Key (SMK) system enables keyless entry and engine start by detecting the authorized key’s proximity through LF and RF communication.
It manages functions like passive lock/unlock, trunk open, start/stop button operation, ESCL control, puddle lamps, and mirror fold/unfold.
The SMK ECU authenticates the key, determines its position (inside or outside), and communicates with the BCM, SSB, and Engine ECU via CAN.
It also provides security warnings like key out, trunk open, or authentication fail.
In my HiL testing experience, I validate these by simulating key positions, antenna signals, and checking CAN message responses for each feature.