## Slide 1: Fault code creation

## Slide 2
Situation: During HIL testing of the Body Control Module (BCM)’s Smart Key system, we needed to verify how the ECU responds to antenna faults that affect key detection inside the vehicle.
Task: My task was to simulate an Interior Antenna fault and ensure the ECU correctly detects it, logs the appropriate Diagnostic Trouble Code (DTC), and prevents unauthorized engine start.
Action: Using the VT HIL setup equipped with a VT2820 relay card, I simulated an open-circuit fault by disconnecting the Interior Antenna 1 line. The Smart Key FOB was kept active, and I attempted to start the vehicle using the Start/Stop button while monitoring ECU responses through CAN logs and diagnostic tools.
Result: The ECU accurately detected the antenna disconnection and stored DTC P16900 – Interior Antenna Fault. The system blocked the engine start for security reasons, confirming that the BCM’s key detection and immobilizer logic performed correctly under fault conditions.
Interior Anteena-1 Not Working
Root Cause / Recommendation Discussion (if interviewer asks follow-up):
If the antenna fault is not detected or the DTC doesn’t log, I would first check:
The antenna wiring and connector continuity between the BCM and LF antenna.
The relay configuration in the VT2820 card to ensure correct channel mapping.
The ECU configuration or variant coding, as some vehicle trims may not have all antennas enabled.
If all hardware is verified, I would analyze CAN logs and UDS data to check if the diagnostic detection threshold or debounce logic needs fine-tuning.

## Slide 3
Smart Welcome Mirror Not Working
Smart Welcome Mirror – Feature Verification (KY LP2 Vehicle)
Situation: During HIL/vehicle validation, we observed that the Smart Welcome Mirror feature did not activate when approaching the vehicle with the key fob. This test was performed on the KY LP2 vehicle to verify feature applicability and functionality.
Task: To confirm whether the Smart Welcome feature (auto mirror unfold upon fob detection within LF range) is implemented and functioning correctly for the KY LP2 variant.
Action:
Set initial vehicle conditions: B+ ON, all doors locked, and vehicle in ARM state.
Ensured distance >10 meters, waited 30 seconds to maintain ARM state.
Brought the key fob within the LF detection range to trigger the Smart Welcome function.
Monitored mirror operation and repeated the test three times to confirm consistent results.
Result: The Smart Welcome Mirror did not activate even after multiple trials. The expected result was that the mirrors should unfold automatically upon detecting the fob in LF range. Further verification is needed to determine whether the Smart Welcome feature is applicable or enabled for the KY LP2 vehicle variant.

## Slide 4
Parking Sensor Front and Rear Fault Creation
Situation: In one of my HIL validation tests for the Body Control Module’s Parking Assist System, I was verifying how the ECU detects and handles front and rear ultrasonic sensor faults. Each sensor should have an individual fault diagnosis and corresponding DTC.
Task: My task was to simulate open-circuit faults for all front and rear parking sensors and check if the ECU correctly identifies and logs the respective DTCs (B121000 to B121700) and displays a proper warning to the driver.
Action: I used the dSPACE VT HIL setup with a VT2820 relay card to disconnect the sensor signal lines, simulating open-circuit faults one by one for each sensor — front left, center left, center right, right, and similarly for the rear sensors. During each simulation, I monitored the CAN logs and UDS fault memory to confirm the ECU’s diagnostic response. After restoring the connection, I verified that the DTC status changed from Active to Stored.
Result: The ECU successfully detected and logged individual DTCs for all sensors (B121000–B121700) and displayed a “Parking Sensor Fault” message on the cluster. Fault detection and recovery worked as per the requirements, confirming that the diagnostic strategy and isolation logic were implemented correctly.
Root Cause / Recommendation Discussion (if interviewer asks follow-up):
In case a DTC doesn’t appear or if a false fault is detected, I’d first check sensor harness and connector continuity, confirm ECU variant coding, and verify HIL relay wiring configuration. If hardware and configuration are fine, I’d escalate it as a software diagnostic threshold or debounce tuning issue to the ECU software team.