## Slide 1: UDS Service 0x19 (ReadDTCInformation

## Slide 2
1. Overview Question
Q: What is UDS Service 0x19 used for?
A:
UDS Service 0x19 (ReadDTCInformation) is used to retrieve Diagnostic Trouble Codes (DTCs) and their related data from an ECU. It helps testers and diagnostic tools identify system faults, their status, and history for troubleshooting and validation.
2. Functional Purpose
--> To read DTCs stored in ECU memory.
--> To get DTC count based on specific status masks.
--> To access extended and snapshot data records.
--> To support OBD requirements and emission-related diagnostics.
3. Commonly Used Sub-functions
Subfunction | Hex | Description | Typical Use
ReportNumberOfDTCByStatusMask | 0x01 | Returns count of DTCs matching status mask | Quick system health check
ReportDTCByStatusMask | 0x02 | Returns list of DTCs and their status bytes | Read active/pending DTCs

## Slide 3
4. Status Byte – DTC Status Mask Bits
Bit | Meaning | Description
0 | testFailed | Test failed at least once
1 | testFailedThisOperationCycle | Test failed in current cycle
2 | pendingDTC | DTC detected but not confirmed
3 | confirmedDTC | DTC confirmed and stored
4 | testNotCompletedSinceLastClear | Test incomplete since last clear
5 | testFailedSinceLastClear | Test failed since last clear
6 | testNotCompletedThisOperationCycle | Test not executed this cycle
7 | warningIndicatorRequested | MIL or warning lamp requested

## Slide 4
5. Request/Response Format Examples
🧩 Example 1: ReportNumberOfDTCByStatusMask (0x01)
Request:
19 01 FF
19 → Service ID
01 → Subfunction (ReportNumberOfDTCByStatusMask)
FF → Status mask (check all DTCs)
Positive Response:
59 01 12 34
59 → Positive response for 0x19
01 → Subfunction echoed
12 34 → Number of DTCs (in hex)

## Slide 5
Example 2: ReportDTCByStatusMask (0x02)
Request:
19 02 FF
Positive :
59 02 03 01 23 45 8A 67 89 0F
59 02 → Positive response
03 → Number of DTCs (3)
Then each DTC with status byte:
DTC1 = 0x012345, Status = 0x8A
DTC2 = 0x67890F, Status = 0xXX …
6. ECU Memory Types for DTCs
Memory Type | Description
Primary Memory | Stores active & historic DTCs
Mirror Memory | Backup of last DTCs after reset
Non-volatile Memory | Keeps confirmed DTCs across power cycles

## Slide 6
8. Typical Interview Questions (with brief answers)
What is a DTC?
→ A Diagnostic Trouble Code identifies faults detected by ECU self-diagnostics.
2. What is the difference between confirmed and pending DTCs?
→ Pending DTCs are detected faults not yet confirmed. Confirmed DTCs are validated after repeated detections.
3. How do you clear DTCs?
→ By sending UDS Service 0x14 (ClearDiagnosticInformation) request.
4. What is the purpose of the status mask?
→ It filters DTCs based on their test status bits.
5. What happens if the ECU is locked?
→ You must perform Service 0x27 (SecurityAccess) before reading or clearing DTCs.
6.What’s the response if no DTCs are stored?
→ Negative Response: 7F 19 11 (SubFunctionNotSupported or conditions not met).